## Slide 1
Abstract
3. Structured light reconstruction concept
6. Scanning process
8. Conclusions and future work
5. Hardware
1. Objectives
Fully Reversed Engineering: Streamlining three-dimensional component digitization, modification, and reproduction
CHSLT – ME
Center for Holographic Studies and Laser μmechaTronics
(a)
To design a system for rapid digitization of physical objects for the purpose of reverse engineering
To create a low cost alternative for expensive digitization solutions
To create a streamlined process for digitization that requires minimal user interaction
The ability to quickly digitize a part allows a designer to easily reproduce a component for which CAD files are not available, or allows the designer to create accessories for such components.
For example, Jay Leno uses the NextEngine 3D scanner to quickly reproduce parts for antique cars whose details have been lost to history.
However, current scanners on the market are costly—the NextEngine, for example, costs $2995.
The goal of this project is to build a full field-of-view digitization system at significantly lower cost.
We tested the binary method through simulating using the open-source software POV-Ray.
A 15 cm radius sphere was scanned and radii were fitted to cross sections of the point cloud.
2. Motivation
7. Results
10. References
9. acknowledgements
Project binary patterns onto object
Capture patterns
Calculate difference between images
Compute pixel indices
Project sinusoidal fringes onto object
Capture patterns
Calculate phase
Convert phase to pixel indices
Calculate angle between optical axis of projector and each point on object
Use camera/projector geometry to recover point cloud
Create mesh from point cloud
Cameras: 2 × Logitech C905 Webcam $100
Projector: 1 × Optoma PK201 Pico $250
Parts: Rapid-prototyped from ABS $ 10
Beam: Aluminum L-beam $ 6
Total cost: $366
Logitech C905 Webcam
2 MP, 2.8μm cell size, 50 mm min. focal length
Optoma PK201 Projector
854 px horizontal resolution, DLP projection, throw ratio 2.2
Position equipment
Camera calibration
Projector calibration
Setup
Single view
Data acquisition
Decoding and triangulation
Point cloud
Combine views
Reposition object
Calculate new orientation
Align point clouds
Mesh
Ryan Muller and Chris Thomas
Advisor: Cosme Furlong Mechanical Engineering Department
Axis | Mean Radius(m) | Standard Deviation (um) | Error (um)
x | 0.149992 | 21.12 | -7.92
y | 0.150002 | 16.12 | 1.94
z | 0.149996 | 25.00 | -3.62
Mean | 0.149997 | 20.75 | -3.20
4. Testing the concept through simulation
Chart: Fitted Radii after removal of outliers
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160 | 165 | 170 | 175 | 180
Z-axis | 0.15 | 0.15 | 0.14996 | 0.14999 | 0.15001 | 0.14999 | 0.15 | 0.15002 | 0.14995 | 0.15 | 0.14998 | 0.15002 | 0.15001 | 0.15005 | 0.15001 | 0.15 | 0.14997 | 0.15 | 0.14995 | 0.15 | 0.14998 | 0.15 | 0.15001 | 0.15005 | 0.15001 | 0.15003 | 0.14997 | 0.15 | 0.14995 | 0.15002 | 0.15 | 0.14999 | 0.15 | 0.14999 | 0.14996 | 0.15
Y-axis | 0.14999 | 0.15 | 0.14999 | 0.15003 | 0.15 | 0.14999 | 0.15 | 0.15001 | 0.14997 | 0.15 | 0.15002 | 0.14999 | 0.14999 | 0.15001 | 0.15002
X-axis | 0.15 | 0.15003 | 0.14999 | 0.14998 | 0.14999 | 0.15001 | 0.14997 | 0.14997 | 0.15002 | 0.14995 | 0.15002 | 0.14998 | 0.14997 | 0.15001 | 0.14999 | 0.14997 | 0.15001 | 0.15001 | 0.14999
The availability of rapid prototyping enhances a designer’s creativity and speed, enabling quicker development of new products. However, because this process relies heavily on computer-aided design (CAD) models it can often be time costly and inefficient when a component is needed urgently in the field. This paper proposes a method to seamlessly integrate the digitization of existing objects with the rapid prototyping process. Our technique makes use of multiple structured-light techniques in conjunction with photogrammetry to build a more efficient means of product development. This combination of methods allows our developed application to rapidly scan an entire object using inexpensive hardware. Single views obtained by projecting binary and sinusoidal patterns are combined using photogrammetric feature tracking to create a computer model of the subject.
Notes: Put the two otoscopes together – may be put a diagram of what’s inside